Layout Documentation

Drawing units are millimeters.

This design and all drawings in this package are provided by Ark Metrica LTD under the following license terms: Attribution-NonCommercial-ShareAlike 4.0 International (CC BY-NC-SA 4.0)
See LICENSE.txt for details

Glass drawing file name: glass.dxf

Nominal dimensions: 30.00 mm square
Final shape tolerance: 0.2mm or better on the “shadow” (2D projection) of the glass piece

Illumination aperture drawing name: light.dxf

light mask holes, nominally:
a: area = 10 mm^2
r: radius = -sqrt(h*w-a)/sqrt(4-π) ~= 0.530959
h: height = 2.845 mm
w: width = 3.6 mm
governing equation: (a-r*r*(π-4))/h = w

nominal geometric dark area
dark area = 15.666 mm^2
found by inspection of the drawing
Active area mask drawing name: active.dxf

Drawing name for areas that must be clean when metal is deposited: clean.dxf

Everything except the two central black rectangles shown here must be clean when metal deposition takes place so that metal is deposited directly onto glass or TCO with no abrorber/ETL/HTL or other device layers in between.
Encapsulation drawing name: encapsulation.dxf

The outer dimensions of the encapsulation glass should be 30mm by 18.84mm. The inner pocket should be 27mm by 15.84mm so that the nominal width of glued region is 1.5mm wide.
Metal mask drawing name: metal.dxf

Pixel #1 indicated by a flat region in the lower left corner.
TCO pattern drawing name: tco.dxf

TCO should remain in the red hatched areas, bare glass in the black areas.